This page was exported from Braindump2go Exam Dumps Free Download [    https://www.pass4surevce.com    ]

Export date: Tue Apr 16 19:09:54 2024 / +0000 GMT

## [210-260 New VCE]Exam Pass 100%!Braindump2go 210-260 Exam Questions 265q Instant Download[91-100]

(2017 June)Cisco 210-260 Exam Dumps with PDF and VCE New Updated in www.Braindump2go.com  Today!

100% Real Exam Questions! 100% Exam Pass Guaranteed!

1.|2017 Version New 210-260 PDF and 210-260 VCE 265Q&As Download:

http://www.braindump2go.com/210-260.html

2.|2017 Version New 210-260 Exam Questions & Answers Download:

https://drive.google.com/drive/folders/0B75b5xYLjSSNV1RGaFJYZkxGWFk?usp=sharing

QUESTION 91

Which type of address translation should be used when a Cisco ASA is in transparent mode?

A.    Static NAT

B.    Dynamic NAT

C.    Overload

D.    Dynamic PAT

Answer: A

QUESTION 92

Which components does HMAC use to determine the authenticity and integrity of a message? (Choose two.)

A.    The password

B.    The hash

C.    The key

D.    The transform set

Answer: BC

QUESTION 93

What is the default timeout interval during which a router waits for responses from a TACACS server before declaring a timeout failure?

A.    5 seconds

B.    10 seconds

C.    15 seconds

D.    20 seconds

Answer: A

Explanation:

Router(config)#tacacs-server timeout ?

<1-1000> Wait time (default 5 seconds)

QUESTION 94

Which RADIUS server authentication protocols are supported on Cisco ASA firewalls? (Choose three.)

A.    EAP

B.    ASCII

C.    PAP

D.    PEAP

E.    MS-CHAPv1

F.    MS-CHAPv2

Answer: CEF

Explanation:

The ASA supports the following authentication methods with RADIUS servers:

PAP - For all connection types.

CHAP and MS-CHAPv1 - For L2TP-over-IPsec connections.

MS-CHAPv2 - For L2TP-over-IPsec connections, and for regular IPsec remote access connections when the password management feature is enabled. You can also use MS-CHAPv2 with clientless connections.

Authentication Proxy modes - For RADIUS-to Active-Directory, RADIUS-to-RSA/SDI, RADIUS- to-Token server

http://www.cisco.com/c/en/us/td/docs/security/asa/asa91/configuration/general/asa_91_general_config/aaa_radius.html#77318

QUESTION 95

Which command initializes a lawful intercept view?

A.    username cisco1 view lawful-intercept password cisco

B.    parser view cisco li-view

C.    li-view cisco user cisco1 password cisco

D.    parser view li-view inclusive

Answer: C

Explanation:

Before you initialize a lawful intercept view, ensure that the privilege level is set to 15 via the privilege command.

SUMMARY STEPS

1. enable view

2. configure terminal

3. li-view li-password user username password password

4. username lawful-intercept [name] [privilege privilege-level| view view-name] password password

5. parser view view-name

6. secret 5 encrypted-password

7. name new-name

QUESTION 96

Which security measures can protect the control plane of a Cisco router? (Choose two.)

A.    CCPr

B.    Parser views

C.    Access control lists

D.    Port security

E.    CoPP

Answer: AE

Explanation:

Table 10-3 Three Ways to Secure the Control Plane

Using CoPP or CPPr, you can specify which types of management traffic are acceptable at which levels.

For example, you could decide and configure the router to believe that SSH is acceptable at 100 packets per second, syslog is acceptable at 200 packets per second, and so on. Traffic that exceeds the thresholds can be safely dropped if it is not from one of your specific management stations.

You can specify all those details in the policy.

You learn more about control plane security in Chapter 13, "Securing Routing Protocols and the Control Plane."

Selective Packet Discard (SPD) provides the ability to

Although not necessarily a security feature,

prioritize certain types of packets (for example, routing protocol packets and Layer 2 keepalive messages, route processor [RP]). SPD provides priority of critical control plane traffic which are received by the

over traffic that is less important or, worse yet, is being sent maliciously to starve the CPU of resources required for the RP.

QUESTION 97

Which statement about extended access lists is true?

A.    Extended access lists perform filtering that is based on source and destination and are most effective when applied to the destination

B.    Extended access lists perform filtering that is based on source and destination and are most effective when applied to the source

C.    Extended access lists perform filtering that is based on destination and are most effective when applied to the source

D.    Extended access lists perform filtering that is based on source and are most effective when applied to the destination

Answer: B

Explanation:

Standard ACL

1) Able Restrict, deny & filter packets by Host Ip or subnet only.

2) Best Practice is put Std. ACL restriction near from Source Host/Subnet (Interface-In-bound).

3) No Protocol based restriction. (Only HOST IP).

Extended ACL

1) More flexible then Standard ACL.

2) You can filter packets by Host/Subnet as well as Protocol/TCPPort/UDPPort.

3) Best Practice is put restriction near form Destination Host/Subnet. (Interface-Outbound)

QUESTION 98

Which protocols use encryption to protect the confidentiality of data transmitted between two parties? (Choose two.)

A.    FTP

B.    SSH

C.    Telnet

D.    AAA

E.    HTTPS

F.    HTTP

Answer: BE

QUESTION 99

What are the primary attack methods of VLAN hopping? (Choose two.)

A.    VoIP hopping

B.    Switch spoofing

C.    CAM-table overflow

D.    Double tagging

Answer: BD

QUESTION 100

How can the administrator enable permanent client installation in a Cisco AnyConnect VPN firewall configuration?

A.    Issue the command anyconnect keep-installer under the group policy or username webvpn mode

B.    Issue the command anyconnect keep-installer installed in the global configuration

C.    Issue the command anyconnect keep-installer installed under the group policy or username webvpn mode

D.    Issue the command anyconnect keep-installer installer under the group policy or username webvpn mode

Answer: C

!!!RECOMMEND!!!

1.|2017 Version New 210-260 PDF and 210-260 VCE 265Q&As Download:

http://www.braindump2go.com/210-260.html

2.|2017 Version New 210-260 Study Guide Video:

YouTube Video: YouTube.com/watch?v=9yy5IlptXYw

Post date: 2017-06-13 07:44:25

Post date GMT: 2017-06-13 07:44:25

Post modified date: 2017-06-13 07:44:25

Post modified date GMT: 2017-06-13 07:44:25

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com